## Slide 1: C Model Implementation
SD1 實習生 賴宥齊
202408
Github

## Slide 2: Outline
Introduction
Comparison
Input & Output
Methods
  Payload Generation
  Length Field Recalculate
  Default Values
TBD
  Advise
  Error Handling

## Slide 3: Introduction
DPTX -> DPIA
  Given DP signal as input, program transforms the input DP signal into USB4 Tunneled Packet.
Script -> DPIA
  Program generates the USB4 Tunneled Packet according to the given packet type and value of each fields.
 | DPTX -> DPIA | Script -> DPIA
Input | DP signal | Self-defined packets
Number of packets | Acc. DP signal | Can be user-defined
Packets order | Acc. DP signal | Can be user-defined
Value of each fields | Acc. DP signal | Can be user-defined
Coverage | Low | High
Additional input file | No need | Need
Output | USB4 Tunneled Packet in txt file | USB4 Tunneled Packet in txt file

## Slide 4: Input
Input Format:
  MSA <Fill Count> <Lane Number>
  BSP <SR> <CP> <Fill Count> <Lane Number>
  VDP <EOC_1> <TU_type_1> <L_1> <Fill_Count_1> <Video_Count_1> ... <EOC_n> <TU_type_n> <L_n> <Fill_Count_n> <Video_Count_n>
  SDP <EFC/ND_1> <NSS_1> <NSE_1> <L_1> <Fill_Count_1> <Secondary_Count_1> ... <EFC/ND_n> <NSS_n> <NSE_n> <L_n> <Fill_Count_n> <Secondary_Count_n>
  Ignore ‘\n’ and ‘#’
Format File
Notes: Explain why lane number needed in MSA and BS.

## Slide 5: Input
Input Format:
  MSA <Fill Count> <Lane Number>
  BSP <SR> <CP> <Fill Count> <Lane Number>
  VDP <EOC_1> <TU_type_1> <L_1> <Fill_Count_1> <Video_Count_1> ... <EOC_n> <TU_type_n> <L_n> <Fill_Count_n> <Video_Count_n>
  SDP <EFC/ND_1> <NSS_1> <NSE_1> <L_1> <Fill_Count_1> <Secondary_Count_1> ... <EFC/ND_n> <NSS_n> <NSE_n> <L_n> <Fill_Count_n> <Secondary_Count_n>
  Ignore ‘\n’ and ‘#’
Format File
Notes: 為何只有MSA跟BSP需要lane number

## Slide 6: Output
Output Format:
  <Valid> <Header> <B0> <B1> <B2> <B3>

## Slide 7: Input & Output

## Slide 8: Input & Output

## Slide 9: Input & Output

## Slide 10: Input & Output

## Slide 11: Method
Flow Chart
Notes: 改成一條龍

## Slide 12: Method
Payload Generation
  (MSA & BS) Payload is generated according to the give number of lanes.
  (VD & SD) Payload is generated sequentially starting from 00 except the padding bytes which are 0.
Length Field Recalculate (VDP & SDP)
  After generating payload of TU sets, recalculate the Length field and HEC.
Default Values
  HopID = 9, Reserved = SuppID = 0
Notes: Padding setting? 給一下enum

## Slide 13: TBD
Advise
  Require any modifications to the input format?
  Are there any other methods for generating payload needed.
Error Handling
  How should the program handle input that does not match the expected format? (e.g. Missing argument)
  Should there be a check to ensure that the sum of Video/Secondary Count fields does not exceed 256?
  Is there a need to set limits for specific input fields?